## Slide 1: People counting example setup guide

## Slide 2: Hardware and software requirements
Hardware requirements:
  Nucleo F401RE
  X-NUCLEO-53L1A1
  Windows PC
SW requirements
  STSW-IMG010
X-NUCLEO-53L1A1
Nucleo F401RE

## Slide 3: STSW-XXX content
Search for STSW-IMG010 on st.com, download and unzip the file in your hard drive C:\
It is strongly recommended to unzip the file in short path like C:\ because KEIL doesn’t support a long path and you may find the error “file not found” when compiling the KEIL example project.
VL53L1X ULD API and other STM32 drivers
Contains binary application file
Precompiled IAR project
Precompiled KEIL project
Precompiled Eclipse project

## Slide 4: Run the example
Plug the expansion board on the F401RE Nucleo board
Connect the F401RE Nucleo board to a PC USB port
Flash the demo application by drag and drop the binary file located in the Binary directory, the demo will start immediately once the FW is loaded
Open a Tera-Term to monitor the people counting (460800 Baud-rate)
Place the board without any object within 2 m in front of the device, wave your arm in front of the sensor from left to right and from right to left at a distance < 1m (figure1), you should see the people counting result displays as below in the Tera term.

## Slide 5: Modifying, compiling and running the example code
The example code is precompiled for the most popular professional IDEs
(KEIL,IAR and Eclipse)
I suppose that you already have your favourite IDE and familiar with.

## Slide 6: Figures
Move your arm in front of the sensor to simulate people walk in and out
Figure1